## Slide 1: Muscle Movement Detection Unit
CPE 301 – Microcontroller Based Systems
Ralph Mago

## Slide 2
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Introduction
Aim:
Accomplishments:
Capture gyro/accelerometer data from muscle movements in the Z-axis, rotation around the X-axis, and rotation around the Y-axis.
Display these movement patterns using a serial terminal with values transmitted wirelessly via Bluetooth.
Because wireless implementation is possible, this device has an application in tracking muscle twitching patterns by storing data into a mobile device.
Fully developed version of this circuit will be similar to a surface electrode which transmits muscle movements to a serial terminal wirelessly.
Successfully paired microcontroller circuit to a serial terminal using Bluetooth
Tested hand movements by rolling left and right along X-axis and pitching up and down along Y-axis. Position of hand is changed along the Z-axis.
  Observed changes in graphs. Three graphs for each axis is displayed.
Completed Schematic and PCB

## Slide 3
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Applications
Applications:
Tracking animal muscle movement:
Diaphragm muscles measured in alligators before diving and during diving. Source: http://jeb.biologists.org/content/211/7/1141
  In the figure to the right the alligator contracts muscles to jump, resulting in a graph spike
  In mid-air, it relaxes, then contracts muscles again diving downwards

## Slide 4
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Applications
Applications:
Tracking muscle twitching patterns:
Muscle stimulation of patients with stages of tetanus. Source: http://www.pef.uni-lj.si/eprolab/comlab/sttop/sttop-bm/bm-elephy.htm
Tension patterns measured with electrodes that send nerve stimuli
  Twitch: Normal muscle contraction
  Summation: Three twitches applied
  Incomplete Tetanus: Abrupt contraction and relaxation
  Complete Tetanus: Long muscle contraction with no relaxation in between

## Slide 5
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Schematic / PCB
ATMega328P has PC4 connected to SDA and PC5 connected to SCL on MPU-6050 (gyro/accelerator)
ATMega328P has RX and TX connected with TX and RX with HC-06 (BT Module)
ATMega328P and MPU-6050 connected to 5V power
BT Module connected to 3.3V power

## Slide 6
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Schematic / PCB
UI represents ATMega328P
M1 represents HC-06 Bluetooth Module
B1 represents MPU-6050 Gyro/Accelerometer

## Slide 7
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Design Stages
Components
Interfaces
ATMega328P
  UART – TX and RX between HC-06 and Serial Terminal
    Serial Terminal used is Bluetooth Terminal/Graphics on Android
  I2C – HC-06 is the slave device
Atmel Xplained Mini (328P) | 1
MPU6050 Gyro/Accelerometer | 1
HC-06 Bluetooth Module | 1
Power Supply (5V) | 1

## Slide 8
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Code Development
This code is a variation of the code found at https://github.com/YifanJiangPolyU/MPU6050 which was created by Yifan Jiang in Hong Kong Polytechnic University for driving the MPU6050.
Includes headers for UART for printing output data into a string
Includes headers for I2C master library for address and transfer direction (same as i2cmaster.h and i2cmaster.c from Dr. Venki
  Both libraries created by Peter Fleury on http://jump.to/fleury

## Slide 9
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Code Development
The “complementary filter” is referenced from http://www.pieter-jan.com/node/11 allows us to read gyroscope data and accelerometer data without noise
Pitch and roll angle values are updated with new gyroscope values by means of integration over time

## Slide 10
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Output
Position along Z-axis (red)
  Graph spikes up when moving left
  Graph spikes down when moving right
Side-to-side rotation about X-axis aka Roll (green)
  Turning around X-axis results in a vector on the Y-axis
  Graph spikes up rolling right
  Graph spikes down rolling left
Up-and-down rotation about Y-axis aka Pitch (blue)
  Turning around Y-axis results in a vector on the X-axis
  Graph spikes up pitching upwards
  Graph spikes down pitching downwards

## Slide 11
University of Nevada Las Vegas. Howard R. Hughes College Of Engineering
Video
http://www.youtube.com